Connections on the 954 wiring loom that are used

Rear & rear brake light switch – use either to connect to the brake light switch.

Neutral switch – Connected to neutral switch input on Digidash.

Alternator – Connects to alternator on engine.

Starter relay / main fuse – I assume this connects to the starter motor.

Rear left signal – Extended to rear left indicator.

Rear right signal – Extended to rear left indicator.

License plate light – Extended to rear license plate light.

Brake tail LED – Extended to rear tail / brake lights. (brown & white for tail – green & yellow for brake).

Fuel injectors + throttle position sensor – Connect to engine.

Fuel pump and warning light – connects to fuel pump.

Engine start / stop switch – Start connected to the savage start switch but the stop wires are joined together.

Ignition coils and sparks – connects to engine (probably needs extending).

Cooling fan switch – connects to fan.

Front right turn – Connected to light and indicator switch in dash via blue.

Front left turn – Connected to light and indicator switch in dash via orange.

Side lights – connects to front side lights and tail lights. Appear to always be on using loom but need to wire side light savage button on dash to allow switching.

Headlight (low) – used for dipped beams (white wire appears to be switch).

Headlights (high) – used for high beams (solid dark blue appears to be switch).

Horn and horn switch – wired to horn and savage horn switch on dashboard.

Turn signal switch – connected to toggle switch on dash (see front signals).

Dimmer switch – connects to high and dipped beam savage switches on dash

Fuse box – this is just used as is.

Engine coolant temp sensor – From engine to loom to provide ECU info. Digidash has it’s own temp sensor as well.

Pulse generator coil – Just connect loom to engine.

Inlet air temp sensor – connect loom to engine.

PAIR Control valve – connect loom to engine.

H-VIX servo  – connect loom to engine.

Cam pulse generator – Connect loom to engine.

Connections on the 954 wiring loom that are not used.

Engine coolant temp sensor – Not used because DigiDash Lite sensor is used.

Oil pressure switch – Not used because DigiDash Lite sensor is used.

Speed sensor – Not used because DigiDash Lite sensor is used.

Side stand switch – connect wires together (green and green-yellow).

Lean angle sensor – not used but outer two wires (red-orange and black) need joining together.

Clutch switch – join together (green-white and green-red I think).

MAP sensor – Not needed.

Oxygen sensor – Not needed.

Purge valve control – Not needed.

Ignition switch – Not used as ignition wired inline with digidash but need a 2000ohm resistor between pink and red to override hotwire security.